## Slide 1
A Rust-Native Embeddable Reactive
Numerical Language for
Heterogeneous Computing in Robotics
Corey Montella, Aung Kant Ko, Steven McPhillimey
www.mech-lang.org
Motivation
Numerical
Extended Kalman Filter
==========================================
+> math/*, logic/all
Δt := 0.1
m := [140 12]'
Q := [0.01 0
0 0.0025]
R := 0.25
I := [1 0 0
0 1 0
0 0 1]
~μ := [55 25 0.4]’
~Σ := [100 0 0
0 100 0
0 0 0.15]
Time Update
------------------------------------------
θ := μ[3]
d := v * Δt
G := [1 0 (0 - d * sin(θ))
0 1 d * cos(θ)
0 0 1]
V := [cos(θ) * Δt 0
sin(θ) * Δt 0
0 Δt]
μ̄ := μ + [d * cos(θ)
d * sin(θ)
ω * Δt]
Σ̄ := G ** Σ ** G' + V ** Q ** V'
Measurement Update
------------------------------------------
δ := m - μ̄[1..=2]
δx := δ[1]
δy := δ[2]
q := δx ^ 2 + δy ^ 2
ẑ := atan2(δy, δx) - μ̄[3]
r := z - ẑ
ν := atan2(sin(r), cos(r))
H := [δy / q, (0 - δx) / q, -1]
S := H ** Σ̄ ** H' + R
K := (Σ̄ ** H') / S[1]
A := I - K ** H
μ₊ := μ̄ + K * ν
Σ₊ := A ** Σ̄ ** A' + (K ** K') * R
μ = μ₊
Σ = Σ₊
Mech offers a concrete syntax for typed matrix equations, illustrated by the bearing-only EKF below.
The kernel is shorter than both the textbook-style Rust implementation and the SIMD Rust implementation. SIMD Rust adds vector and batch support, while Mech reuses one numerical kernel across backends.
Mech compiles this syntax to a typed dataflow artifact that can run in a nalgebra-based interpreter or compile for different host architectures without source changes or backend-specific annotations.
Normalized
Application source | Mech | Rust textbook | Rust SIMD
Setup | 340 | 486 | 561
EKF + candidate update | 356 | 1,024 | 1,119
Validation | 383 | 263 | 396
Matrix helpers | 0 | 251 | 310
SIMD + batch support | 0 | 331 | 2,857
Total | 1,079 | 2,355 | 5,243
The EKF and candidate update alone use about three times as many normalized characters in Rust (1,024 or 1,119) as in Mech (356), before counting helpers or batching.
SIMD and batch support adds 2,857 characters, over half the Rust SIMD source. Mech handles these operations in reusable compiler and runtime components.
Programmer-chosen names count as one character per occurrence. Comments and nonliteral whitespace are removed. General library, compiler and runtime internals are excluded.
Embeddable
Mech runs standalone or embeds in Rust, from a single numerical function to a reactive subsystem. Rust hosts can compile Mech source or load a dylib, and browser applications can embed it through WebAssembly.
JIT compilation from Rust
use mech::kernel::{Backend, Kernel};
let source = include_str!("ekf.mec");
let kernel = mech::mech!(source)
.input("bearing", [-0.55; 4])
.export("state")
.compile(Backend::Jit)?;
let mut ekf = kernel.start()?;
ekf.turn([("bearing", [-0.54; 4])])?;
let state = ekf.state("state")?;
Compile Mech source from a file or inline macro, then submit updates as they arrive. Calls run synchronously.
Checked dylibs
Artifact | Bytes | M/s ± MAD | Peak RSS (MiB)
Mech scalar | 33,544 | 14.671 ± 0.008 | 2.69 ± 0.00
Rust scalar | 50,016 | 21.121 ± 0.005 | 2.69 ± 0.00
Mech SIMD-4 | 33,864 | 34.863 ± 0.010 | 2.69 ± 0.00
Load an AOT library
The bundle stores the dylib and metadata for named inputs, exported state and initial values.
Reactive
Mech models robot feedback loops over continuous sensor streams from Rust host drivers, through direct interfaces or ROS. Each update triggers a turn that computes and validates candidate state. Rejection notifies the caller and preserves prior state.
Build and activation (once)
.mcfg configuration
Activation checks host availability and capabilities (resource permissions).
Heterogeneous
Mech’s typed graph targets CPU/GPU and WebAssembly/WGPU. The right chart runs the same f32 EKF on five backends without source changes. Integrity checks add cost but can be disabled to increase throughput. The left chart compares a similar workload across languages used for numerical computing.
Mech and Rust show similar throughput
Backend choice changes EKF throughput
Median ± MAD
Median ± MAD
Chart: Throughput (million filter-turns/s, linear scale)
| Numba | Futhark | Julia | Mojo | Rust | Mech
Checked | 79.3803 | 97.897 | 129.0474 | 119.2909 | 149.9411 | 151.323
Unchecked | 81.557 | 149.9313 | 136.4017 | 128.1522 | 170.4902 | 184.1365
unchecked (top)
checked (bottom)
Chart: Throughput (million filter-turns/s, logarithmic scale)
| Interpreter | Scalar JIT | SIMD AOT 1w | SIMD JIT 8w | Metal GPU
Checked | 0.69504 | 13.2241 | 34.6166 | 121.0712 | 420.8962
Unchecked | 0.82789 | 15.9487 | 37.0592 | 141.645 | 420.7468
79.4 ± 0.6
81.6 ± 0.3
97.9 ± 1.2
149.9 ± 1.4
129.0 ± 2.8
136.4 ± 1.1
119.3 ± 0.4
128.2 ± 0.2
149.9 ± 2.5
170.5 ± 1.7
151.3 ± 2.6
184.1 ± 8.1
0.7
0.8
13.2
15.9
34.6
37.1
121.1
141.6
420.9
420.7
SIMD JIT and AOT share the numerical compilation pipeline.
1w/8w: one/eight workers. Worker scaling depends on host support.
Performance specialists may further optimize these implementations.
Status and Future Work
Mech v0.4-beta needs further validation and hardening. Over the next year, we plan to expand research-robot deployments and use feedback from users to guide work on additional hosts, an expanded standard library and language features. A v1.0 release candidate is planned for 2028.
✓
Start
Implementation
begins
2018
✓
0.0.1
First alpha
release
2019
✓
v0.1
Proof of
concept
2023
✓
v0.2
Data
specification
2025
✓
v0.3
Program
specification
2026
v0.4
Reactive
Runtime
In progress
v0.5
Distribution
& concurrency
2027 (planned)
v1.0
Release
Candidate
2028 (planned)
Experience this poster as a live reactive program: CPU/WGPU in WebAssembly.
program.mecb
Serialized artifact
ekf.mec
Mech compiler
Program Artifact
(typed dataflow graph)
Activate
Resident computation
encode / decode
Live execution (each turn)
Resident computation
Time update
Measurement update
μ → robot pose
Σ → ellipse
Validate
candidate
Publish state
+ record
pass
Abort candidate
retain prior state
fail
Rust host
drivers
EKF state telemetry
μ = [98.24, 55.19, -0.034]
Σ = [107.89 −28.89 −0.907
−28.89 19.88 0.104
−0.907 0.104 0.012]
SVG scene
Pose and 2σ
position ellipse
Inputs
Program
Outputs
Failures
Activation failed
±
<0.1
±
<0.1
±
<0.1
±
0.5
±
2.3
±
<0.1
±
<0.1
±
0.1
±
0.8
±
2.3
let kernel = unsafe { Kernel::load_bundle("ekf.bundle")? };
let mut ekf = kernel.start()?;
ekf.turn([("bearing", [-0.54; 4])])?;
-- +> import library
-- ~ mutable
-- := define
-- = assign
-- ** matrix multiply
-- ' transpose
-- * broadcast multiply
-- x! integrity constraint
Rust’s memory safety and performance make it a strong foundation for robotics. Numerical kernels can still require substantial code for SIMD layouts and GPU execution. This code can obscure the equations, and each specialized version must be verified and maintained.
Mech is an open-source, Rust-native embeddable language that simplifies numerical code. For robotics, its reactive runtime reduces the host code needed to handle sensor streams, validate updates and recover from rejected turns without losing the last accepted state.
Embedded numerical kernels are one use of Mech’s full language, which also has first-class state machines and pattern matching: see the QR demo below.
Benchmark setup. Apple M1 (4P + 4E, 8-core GPU, 8 GB), macOS 15.6.1. f32, 500,000 filters × 40 turns, n=10. CPU: 8 workers, fused turns. Mech backends: per-turn publication.
Rust 1.96.0-nightly ec818fda3/LLVM 22.1.0. Cranelift 0.131.3. Julia 1.12.6. Mojo 1.1.0/MAX 26.6.0. Futhark 0.27.1/ISPC 1.31.0/LLVM 22.1.8. Python 3.12.14/NumPy 2.2.6/Numba 0.61.2. Clang 17.0.0.
Mech v0.4 development (package 0.3.6). Backend pairs f4b69052c, CPU eedc1c75b, dylibs dab98af1d. iros-workshop-benchmarks, benchmarks/iros-2026.
Dylibs: minimal native-ABI hosts, 1 worker, 10,000 filters × 200 turns, n=7. Whole-process peak RSS. Timing excludes compilation, loading and warmup.
†
†
source characters
mech-lang/mech
‡
variance! := all(Σ₊[[1 5 9]] > 0)
Contributions and bug reports are welcome on GitHub: mech-lang/mech.
‡
Notes: IROS 2026 poster update: factual provenance and comparison scope
Original title/authors/logos/QR retained from the supplied poster. The roadmap follows the current public About Mech page. Future dates are plans, not guarantees.
Repository: https://github.com/mech-lang/mech/tree/iros-workshop-benchmarks
Evidence snapshot: b2522772b280796bfb7c0de39ac9fff235fa9bf8
Ledger: https://github.com/mech-lang/mech/blob/b2522772b280796bfb7c0de39ac9fff235fa9bf8/benchmarks/iros-2026/EVIDENCE.md
CPU values: benchmarks/iros-2026/results/apple-m1-cpu-equal-n10-2026-09-24.json, campaigns.cpu.rows. All 10 fresh-process samples retained; median absolute deviation. 500,000 filters × 40 turns, f32, warm-up excluded. Cross-language fused vs per-turn spectrum publication differs, so the two charts are not interchangeable. Cross-language checked guards use finite checks, positive diagonals, symmetry; positive diagonals do not imply positive definiteness. Numba/Julia/Futhark candidate rejection differs from Mech/Rust block-atomic rollback. These measurements are not a universal language ranking or inferential evidence of a Mech/Rust difference. Mech uses Cranelift, Rust LLVM. Mojo source fingerprint does not match retained fused behavior; its row is archived incomplete-provenance evidence, not a reproducible same-HEAD claim.
AOT: checked, one host thread, 10,000 filters × 200 turns, n=7; common dylib runner, 100 warm-up turns/reset, no compile/load/packing in the timed section. Mech scalar 33,544 B /14.671420±0.007511 M/s; Rust scalar 50,016 B /21.120718±0.004868; Mech SIMD4 33,864 B /34.863147±0.010302. Whole-process peak RSS median all 2,818,048 B (MAD 0); ranges overlap. Rust is specialized scalar with local LLVM vectorization, not equivalent packed SIMD. Scalar Mech is slower than Rust; packed Mech outperformance is a strategy difference. Dylibs contain native selected compute/check machinery, not the full general Mech scheduler. C ABI buffers, not arbitrary Rust shared structures. Source snippet: benchmarks/iros-2026/rust-dylib/dylib-runner.rs.
Source size: benchmarks/archive/compute/parallel-ekf/source-size-audit/selected/ekf.mec and rust_textbook.rs /rust_simd.rs. Names one character, no comments/whitespace; totals 1079/2355/5243. Rust SIMD wrapper1243 +batch/rollback1614=2857. General runtime/compiler internals excluded for both. The full 53-line EKF listing from the user-supplied poster is retained verbatim, including syntax colors. Source-size counts use the checked benchmark .mec with explicit guard expressions. The displayed listing uses the original poster notation. Ordinary nalgebra0.34.2 storage/ops; accelerated compute hot kernels do not call nalgebra.
Versions: Apple M1 8 cores (4P+4E),8GB RAM; macOS15.6.1; Rust1.96.0-nightly ec818fda3 (2026-03-02); Cranelift0.131.3; Julia1.12.6; Mojo1.1.0 8189361e /MAX26.6.0; Futhark0.27.1 /ISPC1.31.0 /LLVM22.1.8; Python3.12.14 /NumPy2.2.6 /Numba0.61.2.
Reactive figure is a conceptual turn contract, not a timing claim about the batched kernel. Effects are staged until accepted. Backend selection graphic intentionally does not claim every experimental backend is exposed through .mcfg today. Stable settings currently auto/cpu/gpu/cpu-scalar/wgpu; JIT/SIMD/AOT/Metal are compiler/registry/benchmark pathways.
The scalar dylib pair uses the same ABI, AoS buffers, host loop, checks, and per-turn publication. Rust is hand-specialized scalar arithmetic compiled by LLVM, distinct from the textbook Rust source-size extract. The scalar difference does not isolate embedding overhead. A matched packed-SIMD Rust dylib is still required to compare equivalent SIMD embedding paths.
Reactive figure: simplified from the user's supplied two-phase paper figure. Build/activation produces a resident instance once. Repeated turns bind sensor inputs, execute the affected graph, validate candidates, publish and record accepted state, and deliver effects after publication. Failed candidates preserve the previous accepted state.
Mech execution revisions: CPU eedc1c75b5a780a92d3f50f094be873f93bca6b9; AOT dab98af1deb65d53cb9f88ee057f34ceb2e74609; Metal 45a21a62d4f0e68adc40bb537a8f26e1d11df7d5. Their Cargo manifests declare package 0.3.6. v0.4 is the integration/development line, not a released 0.4.0 compiler label. Rust LLVM 22.1.0 is retained for the identical full rustc hash ec818fda361ca216eb186f5cf45131bd9c776bb4 in the resident benchmark metadata. ISPC separately reports LLVM 22.1.8. Other systems' unrecorded internal LLVM versions are not inferred.
Typography asset: Fira Code 6.2, https://github.com/tonsky/FiraCode/releases/tag/6.2, SIL Open Font License 1.1. The original full EKF source remains verbatim.
The source table counts normalized source characters, not lines. Every identifier occurrence is normalized to one character; comments and nonliteral whitespace are removed. For these selected checked implementations, Rust SIMD totals 5,243 characters versus Mech 1,079. The 2,857-character SIMD/batch category accounts for most of the 4,164-character difference.
EKF citation: Thrun, Burgard and Fox, Probabilistic Robotics, MIT Press, 2005, §7.4.2, Table 7.2. https://mitpress.mit.edu/9780262201629/probabilistic-robotics/ . The displayed implementation is a bearing-only, one-known-landmark adaptation with Euler motion and Joseph covariance, not the book's identical range-and-bearing pseudocode.
Reactive diagram: RuntimeHostInputDriver and RuntimeIngress accept owned input packets into the host queue. A Rust ROS adapter is an illustrative integration route, not a claim that this evidence branch includes a released Mech–ROS bridge. The .mcfg input supplies host/provider instances, resource grants, runtime limits/durability and supported compute selection. Separate experimental compiler and benchmark pathways remain described above. Diagram is simplified from the user's supplied paper figure.
Status and roadmap: https://about.mech-lang.org, read 2026-09-25. Source milestones: implementation begins 2018, first alpha 0.0.1 in 2019, v0.1 proof of concept 2023, v0.2 data specification 2025, v0.3 program specification 2026, v0.4 runtime currently in progress (site says Soon), v0.5 distribution and concurrency planned 2027, v1.0 stable platform planned 2028. The site identifies active beta development focused on the runtime, with experimental, lightly tested or incomplete parts of the wider platform and advises against critical-system use. Stable embedding API work is retained from the project discussion.
Embedding alternatives: Rust can link mech-runtime and use load_source_program or load_bytecode_program, with configured host providers and grants as required (src/runtime/src/runtime/program/loading.rs:73,201). Hosts can register native function catalogs and Rust input drivers (src/runtime/src/runtime/builder.rs:121,137). The optional AOT path emits a native dylib during fixed-shape backend preparation, before turns run. simd_aot.rs:86-87 emits/reuses and loads the dylib, then prepare creates the session buffers. The configured compute-host route prepares this backend during RuntimeBuilder construction, before coordinator load_compiled_program activates the resident plan (src/cli/commands/run.rs:353-365). Activation is not a required dylib-emission operation.
Artifact emphasis and serialization: the highlighted Program artifact is the typed dataflow representation. The bidirectional .mecb link denotes serialization and validated decoding (src/engine/src/artifact/bytecode.rs:258,427,725). The CLI currently rejects mixed compute bytecode loading, so this conceptual diagram does not claim every compute program can be launched from bytecode in this evidence revision.
The user confirmed that the existing QR destination https://mech-lang.org/iros-r4r-2026/index.html should remain the live-poster address. The endpoint returned 404 during the 2026-09-25 check; content will be published there separately.
Embedding interface: the displayed Rust excerpt is taken verbatim from the POSTER-BEGIN/POSTER-END region of examples/embedded_ekf/main.rs on iros-workshop-benchmarks. Run with cargo run --no-default-features --features kernel-aot --example embedded_ekf. The public mech::kernel module re-exports hosts/gpu/src/embed.rs. Kernel::from_source parses source during compile. input selects live bindings and supplies initial arrays, export selects persistent state by lexical source name. Backend::AotSimd emits and loads a four-instance Cranelift library before start allocates the session. turn validates the complete input packet before binding it, then computes and checks one candidate turn. Integrity failure preserves all previously published state, while valid input values remain bound. state returns a borrowed f32 slice in instance-major, column-major component order. The source file examples/embedded_ekf/ekf.mec uses the benchmark equations and explicit guards with self-contained defaults, without the benchmark's array driver section. The original poster listing at right retains its original notation.
The emitted native library contains the numerical turn function. The Rust host library supplies named bindings, session allocation and publication. This convenience interface does not implement arbitrary pre-existing dylib loading, ROS transport or the full coordinator/effect system. The retained dylib measurements time the earlier common-ABI benchmark runner, not compilation or per-call named input binding in this new interface. See docs/embedding-kernels.md.
Matched Mech backend pairs: benchmarks/iros-2026/results/apple-m1-mech-backend-pairs-n10-2026-09-25.json. Source revision f4b69052cc6d1d618e1c80acac947795ab2e8472. Executable SHA-256 2cd25bc77c5d87a6562cd7c62aa4009e3ccd7fe95af38bde498ce05e701185b1. The five rows now each contain checked and unchecked bars, all using 500,000 filters and 40 timed turns after five warmup turns in the same session. Ten fresh-process samples per case, deterministic interleaving, no outlier removal. Median plus unscaled MAD describes observed sample variability, not a confidence interval. Both modes retain per-turn publication. Unchecked removes only the three named source predicates and their otherwise-dead instructions. Source, inputs and numerical optimizations are shared within each backend pair. Seven source bindings are live in every backend. Compilation, AOT loading, allocation, packing, worker creation, warmup and final host readback are excluded. The new right-hand chart replaces all previous mixed-workload backend values; the left fused cross-language chart and the embeddable section's n=7 common-ABI dylib table retain their separately documented evidence.
The fixed-shape evaluator interprets lowered numerical instructions, rather than running the general source-language interpreter. The kernel-bench Cargo profile optimizes mech, mech-gpu, mech-compute and wide at level 3; source compiler/catalog dependencies remain at level 0, with debug symbols and incremental compilation disabled. Generated Cranelift and Metal code have their own compilation settings. This is not a uniform release profile. See benchmarks/iros-2026/MECH-BACKEND-PAIRS.md.
Preflight: all ten combinations compare every state component over 45 turns at 4,092 instances against the checked scalar evaluator with abs 2e-4 + rel 1e-5 tolerance. All checked paths verify the reported last-lane NaN fault and preserve the complete previously published state. The embedding API's twelve integration tests also pass with the benchmark features enabled.
Complete paired summaries (million filter-turns/s):
{
"evaluator": {
"checked": {
"n": 10,
"median_million_filter_turns_per_second": 0.695042081257192,
"mad_million_filter_turns_per_second": 0.00106619241415834,
"minimum": 0.6914666541027176,
"maximum": 0.6963894080737908,
"samples_million_filter_turns_per_second": [
0.6963119506784141,
0.691474818202843,
0.6914666541027176,
0.6943103467182352,
0.6954768079240193,
0.6963518763439652,
0.6945469192474181,
0.6959045966642866,
0.6963894080737908,
0.6946073545903646
],
"samples_elapsed_ns": [
28722758500,
28923685250,
28924026750,
28805562375,
28757249375,
28721111667,
28795750792,
28739571625,
28719563750,
28793245375
],
"checksums": [
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138
]
},
"unchecked": {
"n": 10,
"median_million_filter_turns_per_second": 0.8278867294891764,
"mad_million_filter_turns_per_second": 0.0010342682130255465,
"minimum": 0.8252878258347235,
"maximum": 0.8294064093323731,
"samples_million_filter_turns_per_second": [
0.8254288291068161,
0.8253607752653016,
0.8277262381964557,
0.8287030600235645,
0.8280472207818971,
0.8274474938954149,
0.8252878258347235,
0.8291389353808394,
0.8284888884047696,
0.8294064093323731
],
"samples_elapsed_ns": [
24229829750,
24231827583,
24162578250,
24134096958,
24153211916,
24170717958,
24233969500,
24121409750,
24140335833,
24113630875
],
"checksums": [
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138
]
}
},
"scalar-jit": {
"checked": {
"n": 10,
"median_million_filter_turns_per_second": 13.224083710585894,
"mad_million_filter_turns_per_second": 0.0053554494577738865,
"minimum": 13.213348055231718,
"maximum": 13.291288195047787,
"samples_million_filter_turns_per_second": [
13.21602531987453,
13.230390242373392,
13.22333429530666,
13.224833125865127,
13.25392099011784,
13.219679343457845,
13.221980746763814,
13.226292944533226,
13.213348055231718,
13.291288195047787
],
"samples_elapsed_ns": [
1513314292,
1511671208,
1512477833,
1512306417,
1508987417,
1512896000,
1512632667,
1512139500,
1513620917,
1504745041
],
"checksums": [
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138
]
},
"unchecked": {
"n": 10,
"median_million_filter_turns_per_second": 15.948693690507435,
"mad_million_filter_turns_per_second": 0.032873735724533226,
"minimum": 15.68643189085235,
"maximum": 15.982320357220843,
"samples_million_filter_turns_per_second": [
15.970489193459889,
15.897644074231627,
15.68643189085235,
15.980435153241887,
15.974050678621442,
15.982320357220843,
15.879842529097784,
15.980814495243093,
15.92689818755498,
15.90943395626059
],
"samples_elapsed_ns": [
1252309792,
1258048042,
1274987208,
1251530375,
1252030584,
1251382750,
1259458333,
1251500667,
1255737292,
1257115750
],
"checksums": [
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138,
133778803.74136138
]
}
},
"simd-aot": {
"checked": {
"n": 10,
"median_million_filter_turns_per_second": 34.61659955143526,
"mad_million_filter_turns_per_second": 0.010267028789513688,
"minimum": 34.29748567276126,
"maximum": 34.6836120760145,
"samples_million_filter_turns_per_second": [
34.641627333538175,
34.61564090426439,
34.61328705684537,
34.627335207970695,
34.60680115039167,
34.62262459236231,
34.605755770145116,
34.617558198606126,
34.29748567276126,
34.6836120760145
],
"samples_elapsed_ns": [
577340083,
577773500,
577812791,
577578375,
577921083,
577656958,
577938541,
577741500,
583133125,
576641209
],
"checksums": [
133778803.74029735,
133778803.74029735,
133778803.74029735,
133778803.74029735,
133778803.74029735,
133778803.74029735,
133778803.74029735,
133778803.74029735,
133778803.74029735,
133778803.74029735
]
},
"unchecked": {
"n": 10,
"median_million_filter_turns_per_second": 37.059153390893584,
"mad_million_filter_turns_per_second": 0.08453453477176254,
"minimum": 35.68238126885224,
"maximum": 37.18796681066932,
"samples_million_filter_turns_per_second": [
37.00580194725714,
35.68238126885224,
36.993934513340825,
37.135500510019895,
37.1518753413108,
37.11250483453003,
36.808455370402136,
37.18796681066932,
37.11343745353572,
36.695143627085606
],
"samples_elapsed_ns": [
540455792,
560500709,
540629167,
538568209,
538330833,
538901917,
543353417,
537808375,
538888375,
545031250
],
"checksums": [
133778803.74029735,
133778803.74029735,
133778803.74029735,
133778803.74029735,
133778803.74029735,
133778803.74029735,
133778803.74029735,
133778803.74029735,
133778803.74029735,
133778803.74029735
]
}
},
"simd-jit-8w": {
"checked": {
"n": 10,
"median_million_filter_turns_per_second": 121.07117587985559,
"mad_million_filter_turns_per_second": 0.5278566332348547,
"minimum": 119.38195959517577,
"maximum": 121.98524893377268,
"samples_million_filter_turns_per_second": [
121.44138783218014,
119.38195959517577,
120.53935382082871,
121.80128880988723,
121.30331263152804,
121.0121153215448,
121.98524893377268,
121.13023643816636,
120.48102047424342,
120.54728467241276
],
"samples_elapsed_ns": [
164688500,
167529500,
165920916,
164201875,
164875959,
165272708,
163954250,
165111541,
166001250,
165910000
],
"checksums": [
133778803.74471432,
133778803.74471432,
133778803.74471432,
133778803.74471432,
133778803.74471432,
133778803.74471432,
133778803.74471432,
133778803.74471432,
133778803.74471432,
133778803.74471432
]
},
"unchecked": {
"n": 10,
"median_million_filter_turns_per_second": 141.64502845825743,
"mad_million_filter_turns_per_second": 0.8321959454704881,
"minimum": 111.9140947408769,
"maximum": 142.53808662217696,
"samples_million_filter_turns_per_second": [
141.3460026467039,
142.3079865020875,
114.72258904929407,
142.53808662217696,
141.94405426981095,
140.79281051087037,
111.9140947408769,
142.45720240181134,
140.15195976237234,
142.03793097379827
],
"samples_elapsed_ns": [
141496750,
140540250,
174333583,
140313375,
140900583,
142052708,
178708500,
140393042,
142702250,
140807458
],
"checksums": [
133778803.74471432,
133778803.74471432,
133778803.74471432,
133778803.74471432,
133778803.74471432,
133778803.74471432,
133778803.74471432,
133778803.74471432,
133778803.74471432,
133778803.74471432
]
}
},
"metal": {
"checked": {
"n": 10,
"median_million_filter_turns_per_second": 420.89616624669395,
"mad_million_filter_turns_per_second": 2.2913551544579036,
"minimum": 415.87174515379456,
"maximum": 424.3394037984699,
"samples_million_filter_turns_per_second": [
423.1927216268747,
418.0445502134316,
418.6100113179589,
424.3394037984699,
420.5634498819794,
415.87174515379456,
418.70092511132003,
421.22888261140844,
421.7177648376493,
424.1530384881557
],
"samples_elapsed_ns": [
47259792,
47841791,
47777166,
47132083,
47555250,
48091750,
47766792,
47480125,
47425083,
47152792
],
"checksums": [
133778803.69828442,
133778803.69828442,
133778803.69828442,
133778803.69828442,
133778803.69828442,
133778803.69828442,
133778803.69828442,
133778803.69828442,
133778803.69828442,
133778803.69828442
]
},
"unchecked": {
"n": 10,
"median_million_filter_turns_per_second": 420.74678044303346,
"mad_million_filter_turns_per_second": 2.282657675358166,
"minimum": 416.0710955659553,
"maximum": 426.6647734128454,
"samples_million_filter_turns_per_second": [
423.62447808140473,
425.918558323605,
419.0591627306884,
426.6647734128454,
421.34498290413796,
416.5849379091606,
416.0710955659553,
421.60960005059314,
420.1485779819289,
420.13717478756814
],
"samples_elapsed_ns": [
47211625,
46957334,
47725958,
46875208,
47467042,
48009417,
48068708,
47437250,
47602208,
47603500
],
"checksums": [
133778803.69828442,
133778803.69828442,
133778803.69828442,
133778803.69828442,
133778803.69828442,
133778803.69828442,
133778803.69828442,
133778803.69828442,
133778803.69828442,
133778803.69828442
]
}
}
}
Memory column: whole-process peak resident set size from apple-m1-aot-vs-rust-dylib-2026-09-24.json, measured by /usr/bin/time -l in seven fresh common-loader processes per artifact. All three medians are 2,818,048 bytes = 2.6875 MiB, with MAD zero; shown as 2.69 ± 0.00 MiB. This includes loader, buffers, library and runtime. It is not incremental dylib memory, and the data do not establish a memory advantage.
Every pair has unchecked above checked. All five Mech rows use examples/embedded_ekf/ekf.mec, SHA-256 da531cddcb25d002d49f1a77800122e84b573e2685e191c1955908ef6fccd625. The preserved source figure uses the original notation, while the measured source version specifies f32 and the integrity predicates.
Textbook source: the authors' official corrected pages204–206, https://robots.stanford.edu/probabilistic-robotics/corrections1/pg204-206.pdf, Table7.2 on page204. Comparable in scale is a qualitative observation about matrix-level expression, not a measured equality of character or line counts. The preserved source is a bearing-only, single-known-landmark adaptation with Euler motion and Joseph covariance. The book's example uses range-and-bearing, a nonlinear velocity motion model and feature iteration.
Dylib size diagnostic, 2026-09-25: rebuilding rust-ekf-dylib.rs with its exact recorded source SHA, rustc ec818fda3 and build flags reproduces50,016 bytes, though its binary SHA differs because of build/install identity. This Rust file contains1,528 bytes of __text. A retained33,864-byte Mech SIMD artifact contains3,636 bytes of __text. Rust has an extra16,384-byte __DATA segment with24 bytes of lazy-linking data, whereas Mech has no __DATA segment. __LINKEDIT is864 bytes for Rust and1,096 for Mech, accounting for the16,152-byte file difference. Rust uses lazy binding and macOS11.0 deployment target; Mech uses chained fixups and target15.0. Both depend only on libSystem. Exact earlier Mech binaries were not retained, so this diagnosis compares a reproduced Rust build with a retained same-size Mech SIMD artifact. The disk-size result should not be interpreted as an inherent language/code-size advantage.
SIMD JIT/AOT: hosts/gpu/src/batched/simd_jit.rs and simd_aot.rs consume the same fixed-shape compute graph and use Cranelift for vector code generation. They have separate lowering implementations, math helper implementations and native dispatch ABIs. The chart compares eight-worker JIT and one-worker AOT, and does not establish equal throughput. JIT compiles to executable memory when requested. AOT emits a relocatable object and links a native library. The minimal Rust common-ABI loader can deploy that library without Mech's compiler. The displayed Kernel::from_source(...).compile(...) example still invokes compilation in its host.
Browser execution: src/wasm/Cargo.toml compiles the Rust runtime wrapper to WebAssembly. src/wasm/src/mixed_compute.rs, gpu.rs and include/browser-compute.js implement browser CPU evaluation and WGPU/WebGPU execution using generated WGSL. This is not a claim of standalone Mech-source-to-Wasm AOT code generation. The QR destination is the user-approved planned live poster and CPU/WGPU comparison at https://mech-lang.org/iros-r4r-2026/index.html. It returned HTTP 404 on 2026-09-25 at 15:06 UTC and still requires publication before distribution.
Chart display precision: data values and bar lengths retain the existing evidence. Labels use one decimal at or above one million filter-turns per second, and two decimals below one. MAD uses the same resolution, with a less-than threshold when rounding would display zero. MAD describes observed run-to-run variability, not measurement accuracy or a confidence interval. Both native horizontal value-axis titles state throughput units and the linear or logarithmic scale.
Reactive output example: the current diagram uses turn800 of the same repeated-input checked Rust f32 control fixture archived in benchmarks/iros-2026/poster/reactive-output/turn-800.json. It is an illustrative state, not a new throughput sample or a freshly executed Mech result. Mean [98.23776245117188,55.18589401245117,-0.034165628254413605]. Covariance rows [[107.88896942138672,-28.88761329650879,-0.9072326421737671],[-28.88755226135254,19.884502410888672,0.10412274301052094],[-0.9072338342666626,0.10412327200174332,0.012010792270302773]]. Matching 2-sigma positional semiaxes [21.58926311865064,6.7080254414225955], SVG rotation 16.642502461815663 degrees. Robot heading -0.034165628254413605 radians. Independent NumPy f32 matrix-equation cross-check is recorded in the same evidence file. The scene is a local view centered on the mean with equal x/y scale. The simplified build/activation lane intentionally omits the separate AOT emission path. The embedding section continues to describe AOT. Rust logo © Rust Foundation, CC BY4.0, recolored white. Source: https://github.com/rust-lang/rust-artwork/blob/main/logo/rust-logo-single-path.svg . License: https://creativecommons.org/licenses/by/4.0/ .
2026-09-25 integrated interface and poster revision: JIT excerpt from examples/embedded_ekf/main.rs; saved native bundle loader from examples/embedded_ekf/load.rs; separate AOT producer in examples/embedded_ekf/build.rs. Backend::Jit compiles scalar Cranelift code once and supports independent persistent sessions. Kernel::save_bundle saves the AOT dylib and interface metadata. Unsafe Kernel::load_bundle loads trusted matching native code without parsing, lowering, compiling or linking. The current Cargo consumer feature still includes compiler dependencies. Public Session::turn reports integrity errors without changing published state and retains updated input bindings on rejection. The Rust crate links into host applications; a generated-kernel rlib export and C++/Python wrappers are not implemented here. New wrapper operations are separately tested, not remeasured in the archived minimal-ABI dylib table. Optional predicates are omitted from the unchecked benchmark source, not disabled via a public Session flag. Benchmark evidence: benchmarks/iros-2026/MECH-BACKEND-PAIRS.md and results/apple-m1-mech-backend-pairs-n10-2026-09-25.json. SIMD AOT throughput reduction is 100*(1-34.617/37.059)=6.59%; Metal checked/unchecked difference is smaller than either MAD. These measure predicate checking, not the complete cost of reactive publication. Interpreter means fixed-shape numerical instruction interpretation, with unchanged measurements 0.695 checked and 0.828 unchecked million filter-turns/s, now displayed to one decimal. Original source and title whitespace restored from the user-supplied PowerPoint. All equations and syntax colors retained. Timeline labels Reactive Runtime and v1.0 Release Candidate, 2028 planned, and the next-year robot-hardware/deployment validation plan are supplied by the user in this revision.
2026-09-25 layout revision: Mech code indentation is one Fira Code space, while import and headings retain their margin. A six-line notation key uses Mech comment syntax in the code panel's upper-right whitespace. Normalized source-character heading and local definition use matching asterisk markers. Reactive legend moved under the paragraph. Activation checks existing configured capabilities and host availability before creating the resident instance, distinct from per-turn integrity validation. Code references: src/runtime/src/runtime/builder.rs:355, src/runtime/src/runtime/program/external/admission.rs:95, src/runtime/src/runtime/program/loading.rs:401. Same-source and checked/unchecked findings promoted to body text without changing data. JIT/AOT pipeline sentence moved below charts. Avenir Next is a body-prose design comparison, with Fira Code headings/code and Segoe UI chart measurements retained.
GitHub Invertocat logo: GitHub Brand Toolkit, https://brand.github.com/foundations/logo. Original white asset: https://brand.github.com/GitHub_Logos.zip.